Absolute Magnetic

Miniature 30 mm Size

Rotary Encoder

Key Benefits & Features

- Robust construction

- Contactless rotary position sensor over 360°

- Immune to external magnetic stray fields

- 14-bit resolution

- Temperature range: -40°C to +85°C

- IP69K Protection

Applications

- Robotic joint position detection

- Industrial motor position control

- Medical robots and industrial equipment

- High-pressure, high-temperature operating conditions

General Description

The SMS is a magnetic Hall sensor system manufactured for heavy operation condition. A lateral Hall sensor array is used to measure the magnetic field components perpendicular to the surface of the sensor. The SMS is uses self-calibration methods to eliminate signal offset and sensitivity drifts. The integrated Hall sensors are placed around the center of the device and deliver a voltage representation of the magnetic flux Bz. Through Sigma-Delta Analog-to-Digital Converter (ADC) and Digital Signal-Processing (DSP) algorithms, the SMS provides accurate high-resolution absolute angular position information. This is executed by a Coordinate Rotation Digital Computer (CORDIC) which calculates the angle and the magnitude of the Hall array signals. A small diametrically magnetized (two-pole) standard magnet provides the angular position information. Depending on the system requirements different magnet diameters are possible. Additional flexibility is given by the wide range of the magnetic input range. The encoder module consists of a magnetic actuator and a separate sensor board. Output signal are provided in industry standard RS-485. The sensor can be operated in two modes: encoder and odometer.

3DTechnologies SMSTM Technical Specifications

| System data |  |
| --- | --- |
| Reading type | Axial reading |
| Resolution | Absolute – to 14-bit resolution per revolution |
| System accuracy | 0.02° |
| Maximum sampling rate | < 10 kHz |
| Communication Interface | Asynchronous serial RS-485 |
| Communication Protocol | Modbus RTU |
| Sensor Output Noise | 2.73LSB@14bit, rms value Max 0.06° |
| Electrical data |  |
| Supply voltage | 5 VDC ± 10% |
| Set-up time | 10 ms (after switch-on) |
| Power consumption | Max 30 mA |
| Environmental data |  |
| Temperature | Operation | -40 °C to +85 °C |
|  | Storage | -50 °C to +110 °C |
| Degree of protection | IP69K (Protected against close-range high pressure, high temperature spray downs) |

Status indicator LED

| LED | Status |
| --- | --- |
| Green | Ready to work, sufficient saturation magnetic field |
| Red | Fault, incorrect placement of the magnet or insufficient saturation magnetic field or another errors |
| Green flashing | Correct work, correct communication |
| Red flashing | Incorrect work, but correct communication |
| No light | No power supply |

Communication Command Package

The sensor can be operated in two modes: Encoder and Odometer. In the Encoder mode, the sensor collects data about the angle, processes the data and provides for the industrial protocol ModBus RTU. In the Odometer mode, besides, SMS  calculates distance traveled and speed. The sensor operates on the ModBus RTU protocol at rates up to 3 Mbit/s, with the RS485 interface.

You can find a detailed description of the format of requests and responses for the respective functions in the «Modbus Application Protocol».

http://www.modbus.org/docs/Modbus_Application_Protocol_V1_1b3.pdf

Service operations for configuring and updating sensor firmware are performed using custom function code (classified information) using the software of "3-D technology."

Read Data Package

For data collection and sensor settings, it has a register file that can be accessed using the standard Modbus functions.

To request information used function 0x03 Read Holding Registers.

Write Data Package

To set values in the SMS registers used function 0x10 Write Multiple registers.

In odometer mode.

To install the odometer distance record in Holding Register with the address 0. It is not necessary to record all the bytes 64-bit value, the missing bytes are filled with zeros automatically.

Record other registers function Write Multiple Registers possible but pointless.

Transmission Errors

In keeping with «Modbus Application Protocol», sensor generates standard responses about error (Exception Code from 1 to 4).

Selecting the Operation Mode (Encoder or Odometer)

Sensor Address

You can set Sensor address (and baud rate) in the settings.

In the settings can be set of a mask that is superimposed on the address in the received packet before checking (for example, it is possible to mask address hub).

If you set the address «0», the sensor sends response package with the same address as in the request.

Register Description

The byte order - Little Endian, but inverting the bytes in registers can be set in the settings.

Register addresses

| Register address Encoder mode | Register address Odometer mode | Data type | Description |
| --- | --- | --- | --- |
| - | 0 | uint64 | Package Odometer data: Bytes 0 - 4: distance in impulses (8192 impulse per revolution), uint64; Bytes 5-6: Speed (0.001 rev/s), int16; Byte 7: Flags: 0x80 - Scan (since the last poll passed given scanning distance). |
| monitor0 | 4 | uint16 | The angle value (14-bit code) |
| 1 | 5 | uint16 | Diagnostic flags (bits): 0-7: Automatic Gain Control value. 0 decimal represents high magnetic field; 255 decimal represents low magnetic field. 8: OCF (Offset Compensation Finished), logic high indicates the finished Offset Compensation Algorithm. After power up the flag remains always to logic high. 9: COF (Cordic Overflow), logic high indicates an out of range error in the CORDIC part. When this bit is set, the angle and magnitude data is invalid. The absolute output maintains the last valid angular value. 10: Comp Low. High level of magnetic field (Indicates a high magnetic field. It is recommended to monitor in addition the magnitude value.) 11: Comp High. Low levels of magnetic field (Indicated a weak magnetic field. It is recommended to monitor the magnitude value.) 14: Error checking settings. 15: CRC error checking. |
| 2 | 6 | uint16 | The angle value (in degrees) |
| 3 | 7 | uint16 | Firmware loader version |
| 4 | 8 | uint32 | Firmware version |
| 6 | 10 | uint32 | Version data formats |
| 8 | 12 | char[16] | Reserved |

Default Settings

| Encoder settings |
| --- |
| Parameter | Value |
| Address | 0 |
| Address mask | 0x1F |
| Bit rate | 3 Mbit/s |
| Reverse the bytes in registers | Disable |
| Sensor resolution | 14 bits |
| Averaging interval (points) | 4 |
| Odometer settings |
| Mode | automatic (for data averaging) |
| Calculation of additional parameters | enabled (reserved) |
| Impulse per revolution | 128 |
| Wheel diameter (mm) | 99 (reserved) |
| Sampling rate (Hz) | 8192 |
| Interval rate averaging | 8192 |

Mechanical Specification

Figure 1:

Installation drawing and physical placement of the magnet

DIMENSION: mm

Cable and connectors specification

| Lemo connector (FVG.03.304.SLAC45) | Male cable connector M5 x 0,5 | Male angled cable connector M5 x 0,5 | Free ends |
| --- | --- | --- | --- |
|  |  |  | RS-485 D+ (DATA A) - Yellow RS-485 D– (DATA B) - Green 5VDC – White Ground - Brown |

Cable and connectors specification

Lemo cable (040 281) with connector (FVG.03.304.SLAC45)

как-то плохо((

IP69K Protection (up to 120 bar pressure)

2 meters cable

1 Pin: 5 VDC 2 Pin: RS-485 D+ (DATA A) 3 Pin: GND 4 Pin: RS-485 D- (DATA B)

Male cable connector M5 x 0,5

IP67 Protection

5 meters cable

1 Pin: 5 VDC 2 Pin: RS-485 D+ (DATA A) 3 Pin: GND 4 Pin: RS-485 D- (DATA B)

Male angled cable connector M5 x 0,5

Male angled cable connector M5 x 0,5

Ordering & Contact Information

| Example: | SMS | E | 8 | 30 | 9 | L |
| --- | --- | --- | --- | --- | --- | --- |
| Device family |  |  |  |  |  |  |
| SMS = Sensor of measuring system |  |  |  |  |  |  |
| Operation mode |  |  |  |  |  |
| E = Encoder O = Odometer |  |  |  |  |  |
| Internal sampling rate |  |  |  |  |
| 1 = 1024 Hz 2 = 2048 Hz 4 = 4096 Hz 8 = 8192 Hz |  |  |  |  |
| Bit rate communication |  |  |  |
| 1 = 9 600 bit/s 2 = 28 800 bit/s 3 = 57 600 bit/s 4 = 115 200 bit/s 5 = 500 kbit/s 10 = 1 Mbits/s 20 = 2 Mbits/s 30 = 3 Mbits/s |  |  |  |
| Impulse per revolution (only Odometer mode) *If you choose Encoder mode, select in this item “–“ |  |  |
| 1 = 2 2 = 4 3 = 8 4 = 16 5 = 32 6 = 64 7 = 128 8 = 256 9 = 512 10 = 1024 |  |  |
| Cable |  |
| L = Lemo connector (FVG.03.304.SLAC45) M = Male cable connector M5 x 0,5 MA = Male angled cable connector M5 x 0,5 F = Free ends |  |

Ordering & Contact Information

| Example: | SMS | E | 8 | 30 | 9 | L |
| --- | --- | --- | --- | --- | --- | --- |
| Device family |  |  |  |  |  |  |
| SMS = Sensor of measuring system |  |  |  |  |  |  |
| Operation mode |  |  |  |  |  |
| E = Encoder O = Odometer |  |  |  |  |  |
| Internal sampling rate |  |  |  |  |
| 1 = 1024 Hz 2 = 2048 Hz 4 = 4096 Hz 8 = 8192 Hz |  |  |  |  |
| Bit rate communication |  |  |  |
| 1 = 9 600 bit/s 2 = 28 800 bit/s 3 = 57 600 bit/s 4 = 115 200 bit/s 5 = 500 kbit/s 10 = 1 Mbits/s 20 = 2 Mbits/s 30 = 3 Mbits/s |  |  |  |
| Impulse per revolution (only Odometer mode) *If you choose Encoder mode, select in this item “–“ |  |  |
| 1 = 2 2 = 4 3 = 8 4 = 16 5 = 32 6 = 64 7 = 128 8 = 256 9 = 512 10 = 1024 |  |  |
| Cable |  |
| L = Lemo connector (FVG.03.304.SLAC45) M = Male cable connector M5 x 0,5 MA = Male angled cable connector M5 x 0,5 F = Free ends |  |

# Text boxes

IP67 Protection

5 meters cable

1 Pin: 5 VDC 2 Pin: RS-485 D+ (DATA A) 3 Pin: GND 4 Pin: RS-485 D- (DATA B)

5 meters cable

Yellow: RS-485 D+ (DATA A)

Green: RS-485 D- (DATA B)

White: 5 VDC

Brown: GND

«3DTechnologies.Ru» Ltd

Russian Federation, Saint-Petersburg,

Bolshoy Sampsonievskiy pr. 60

Tel. +7 (812) 309-22-02

E-mail: info@okb3d.com

http://www.okb3d.com